Convection Heat Transfer over a Cylinder

Free Convection:

First, calculate the Rayleigh number using Equation [1],

[1]

where g is the acceleration of gravity, β = 1/Tf  is the volumetric thermal expansion coefficient for gases, Tf  = (Ts + Ta)/2 is the film temperature, Ts is the surface temperature, Ta is the ambient temperature, D is the cylinder diameter, ν is the kinematic viscosity, and α is the thermal diffusivity.

Note: Make sure that you convert your film temperature to Kelvin before calculating β. Evaluate all air properties at Tf.

Now, calculate the average Nusselt number using Equation [2] and Table [1],

[2]

Table [1]

From Equation [2], you can solve for the convection heat transfer coefficient (h) and use it to calculate the convection heat transfer rate using Equation [3],

[3]

Finally, the total heat transfer from the surface of the cylinder is then equal to the heat transfer by convection and radiation,

[4]

Forced Convection:

First calculate the Reynolds number using Equation [5],

[5]

where ν is the kinematic viscosity, V is the flow velocity, and D is the diameter of the cylinder.

Now, using Equation [6] and Table [2], calculate the average Nusselt number,

[6]

Table [2]

Finally, calculate the convection and radiation heat transfer rates from Equations [3] & [4], respectively.

Note: All properties of air should be evaluated at the film temperature (Tf). Use your heat transfer book to get the properties.