Water Circuit Sample Calculations & Equations

- From your textbook, use Table A.8 to find the density and dynamic viscosity of water:

→  Density of water at room temperature (20°C)

→  Dynamic viscosity of water at room temperature (20°C)

- Calculate the inside diameter of the pipe using the measured outside diameter as follows:

→   where Di is the inside diameter, Do is the outside diameter and t is the wall thickness of the pipe ( t = 0.045 in for the copper pipes in the circuit)

If the measured outside diameter is 1.133 inches then the inside diameter will be 1.088 inches which is equivalent to 0.0276 meters.

- Calculate the average velocity in the pipe:

→  Inside cross-sectional area of the pipe

→  Using the inside diameter calculated above (Di = 0.0276 m)

→  Volumetric flow rate

→  Average velocity in the pipe

- Calculate the Reynolds number (Re):

If Re < 2300 then the flow in the pipe is laminar

If Re > 2300 then the flow in the pipe is turbulent

→  Flow is Turbulent

- Find the friction factor ( ƒ ) using the Moody diagram (Fig. 8.12 in your textbook):

→  Assuming a smooth pipe

- Calculate the pressure drop in a 24 inch straight pipe segment:

The total pressure drop in a water circuit is given by:

where

→  This equation gives the major head loss in a pipe

→  These equations give the minor head loss in fittings and valves

For a straight pipe segment, the pressure drop between two points which are at the same elevation is given by:

→  Note that there are no minor losses or pressure drop due to elevation difference

Therefore, the pressure drop in a 24 inch (0.6096 m) straight pipe segment is:

→  Pressure Conversions

- Calculate the minor losses in pipe fittings using the following tables and figures from your textbook:

Fig. 8.14  →  Use this figure to find the loss coefficient (K) for flow through sudden area changes

Table 8.4 →   Use this table to get the equivalent lengths (Le / D) for valves and fittings

- Obtain the pressure drop across the turbine flow meter using the table provided below:

The above table is taken from http://www.Omega.com/.