Introduction to Mechanical Engineering Contest

The University of Texas-Pan American

Fall 2009

Spaghetti-Bridge

Your team is requested to design and build a well-tested bridge made from spaghetti and glue/epoxy.  The object is to construct a bridge that will carry the heaviest load while still meeting specifications.  Bridges will be loaded until they fail.  A design report must be turned in the day of the contest.  These reports represent 50% of your project grade.  The remaining 50% of your grade will depend on your final ranking in the contest.

Design Contest Parameters

- The bridge is to be built from spaghetti (cylindrical forms of pasta) and glue, epoxy or resin.

- The bridge shall be free-standing and must span two level surfaces which are one meter apart.

- The support for the bridge shall be from the top of the level surfaces.  The edges of the level surfaces cannot be used in any way for support.

- The bridge must include a decking of spaghetti to provide a suitable road surface at least 5 cm wide across the full span of the bridge.  Three conditions must be met:

- Gaps in the bridge deck are not to exceed 2 mm.

- A block of wood (5 cm x 5 cm x 10 cm) representing a car must be able to move along the length of the  decking unobstructed from end to end.

- The deck of the bridge must not be more than 5 cm above or below the ends of the bridge at any point along its length.

- You must incorporate a "loading platform" consisting of a U-bolt secured to a piece of plywood (0.7 cm x 5 cm x 10 cm).  This platform is to be attached at the center of the bridge such that the bottom of the U-bolt is no more than 5 cm from the top of the bridge decking.  All loads will be suspended from this U-bolt, and there must be a clear space directly below it to allow loads to be attached.  Loads will be attached using an S-hook, and, if necessary, a 10 mm diameter metal rod extension.  If during loading, the bridge twists in such a way as to cause the bridge to touch the rod at any point other than the U-bolt, thus lending additional support, the bridge will be disqualified.

- The maximum vertical depth of the bridge, from the highest point in its structure to the lowest cannot exceed 50 cm.

- The maximum weight of the bridge including the loading platform must not exceed 0.75 kilograms.

Note:  These rules are essentially the same as those developed for contests at Okanagan University.  For a bridge meeting these restrictions, Okanagan claims a world record of 176 kg.