## Name: _____________________________________     Date: ____________     Section: _______

MECE 1101 Introduction to Mechanical Engineering – Fall 2009

Homework #5

- If an object having a mass m is raised to a height h above a horizontal surface and then released, the velocity upon impact with the horizontal surface can be calculated as  where g is the acceleration of gravity. Is this equation dimensionally consistent?

- In fluid mechanics, the frictional force of a fluid acting against a smooth surface is given by the equation  where F = frictional force, c = coefficient of friction, ( = fluid density, a = surface area, and v = fluid velocity. What are the dimensions of the coefficient of friction?

- Convert 3 km/hr to inches/sec

- Convert 9.5 km/sec to mi/hr

- Convert 69.12  to

- Convert 1,154 gallons per minute (gpm) to. [ 1 ]

- Convert 1.24 MPa to psi ()

- What is the weight of a 100  mass (a) at sea level where g = 32.174 ft/s2 and (b) in a mountain top where g = 31.925 ft/s2?

- An astronaut weighs 123.4  on Earth. How much will she weigh on Mars where the acceleration of gravity is 12.279 ft/s2?

- Rather than write extremely large numbers or very small numbers, we use prefixes that have been defined for the SI system. Match the prefix with the multiplication factor:

(1) mega, (2) micro, (3) mili, (4) deci, (5) kilo,

(6) hecto, (7) centi, (8) giga, (9) nano, (10) deka

(    ) 1,000,000,000       	(    ) 0.01	(    ) 1,000	(    ) 100	(    ) 0.000001

(    ) 1,000,000                (    ) 0.1           (    ) 0.001	(    ) 10	            (    ) 0.000000001