## Name: ___________________________________________       Date: _______________________

### MECE 1101 – Introduction to Mechanical Engineering

Review – Problem Solving Using Common Engr. Concepts

Objective:

Practice how to set up engineering calculations and how to deal with common physical quantities and concepts.

Problems:

- Robert lives 65 miles from you. You both leave home at 3:00 pm and drive toward each other on the same road. Robert travels at 40 mph, and you travel at 50 mph. At what time will you pass Robert on the road?

- A rectangular tank 10 feet wide, 30 feet long, and 12 feet high is completely filled with gasoline. The gasoline is to be pumped into a spherical tank that is 6.0 meters in diameter. The pump moves gasoline at a rate of 30.0 gallons/minute. (a) How long, in hours, will it take to transfer the gasoline? and (b) what percentage of the spherical tank will be filled with gasoline?

- Juan and Charles are commercial painters. Juan has a job to paint a water storage tank that is a sphere supported above the ground by three legs. The sphere is 15.5 meters in diameter. Charles has a job to paint a gasoline storage tank that is a cylinder 48.0 feet in diameter and 39.0 feet high. The bottom of the tank sits on a concrete pad, and therefore, will not be painted. Juan has bet Charles that he will complete his job first. Assuming that Juan and Charles both paint at a rate of 150 feet square / hour, who will win the bet?

- A liquid mixture of benzene and toluene contains 50% benzene by mass. The mixture is fed continuously to a distillation apparatus that produces vapor containing 60% benzene and a residual mixture containing 37.5% benzene, each by mass. The still operates at a steady state. If the mixture feed rate is 100 kg/hr, determine the mass flow rates for each stream.

- Estimate the total amount of coolant in gallons wasted by a radiator that drips continually at the rate of one drop every two minutes for six months. State all your assumptions clearly.