## Slide 1: Branch Prediction
Dr. Abraham
UTRGV

## Slide 2: Control Hazards
There are two types of branch instructions: conditional and non-conditional
When Branch instructions are executed Program Counter will get a new value
The new value for the PC will not be available until the 4th cycle. Mean while the PC will be updated every cycle. This causes a WAR hazard, as the correct value is written later in the 4th cycle.
Thus three instructions in the pipeline will have to be flushed. To avoid flushing, we can add 3 NOOP for every branch. Very inefficient!!
If we move the branch evaluation to 2nd stage instead of 4th stage (this can be done by adding a OR gate), we will only need to flush one instruction or have one NOOP. Still not very efficient. What other ways can we handle it?

## Slide 3: Possible solutions to Branch Hazards
Insert a non dependent instruction like load or store
Add branch prediction
  Static branch prediction
  Dynamic branch prediction

## Slide 4: Static Branch prediction
Its like a coin toss where one always chooses heads.
Assume branches are never taken
  Conversely assume branches are always taken
There are forward branches and backward branches, here also you can assume one way or another: Assume forward branches (if statements) are never taken, but backward branches (loops) are always taken.

## Slide 5: Dynamic Branch Prediction
If in one instruction branch is taken then assume branch will be taken for the next branch instruction. 1 bit branch prediction. This is the simplest. But does not work well for nested loops. 90% accuracy
Keep tract of previous two or three branch instructions and modify future branch predictions accordingly (2 or 3 bit branch prediction, solves the nested loop problem) -93% accuracy
Another alternative is to analyze the type of instruction that is being executed and modify branch prediction based on the type of instruction.
Yet another way is to keep history and analyze some of the surrounding instructions (new CPUs do this). This increases the accuracy of branch prediction. 96% accuracy

## Slide 6: Instruction Level Parallelism
Issue multiple instructions concurrently
Several instructions being fetched, decoded, executed at the same time
Static Multiple Issue- Longer instruction words (LIW) or (VLIW). These instructions are split and placed in issue slots. GPUs use this
Dynamic Multiple Issue – Processor decides how many instructions to pull at any given clock cycle. Superscalar processors using Tomasulo’s algorithm. Modern CPUs us this.