## Slide 1: Chapters 9,10,11
Dr. Abraham
Professor UTPA

## Slide 2: Already discussed
These chapters were discussed in previous lectures.
A summary is given here

## Slide 3: Chapter 9 Transmission modes
Parallel transmission
  Faster. More wires required including controls.
Serial Transmission
  Replacing parallel as computers are faster now. Less prone to errors and longer cable lengths. Parallel data has to be converted to serial using UART.
Transmission order, MSB or LSB (UART is little endian generally).

## Slide 4: Asynchronous and Synchronous transmission
Asynchronous: RS-232 – see handwritten notes
Synchronous – sender and receiver are always synchronized, does not require start and stop bits.

## Slide 5: Bytes, Blocks and Frames
Sending bytes can be slow. What happens if data is not available to send at all times.
Framing: collect a block of data and then transmit together. Idle bytes and frame start bits are added.

## Slide 6: Simplex, half duplex and full duplex transmission
Simplex – transfer data only in one direction (broadcast radio).
Half duplex: shared transmission medium so only one way at a time. Like walkie talkies.
Full duplex – two channels for sending and receiving.
DCE and DTE see my handwritten notes.

## Slide 7: Modulation and Modems Chp 10
Carriers, Frequency and Propagation. A frequency that will propagate for needed length is used and then data is added to it. Refer to AM, FM, PSM from my notes.
Also refer to modem related notes.

## Slide 8: Chapter 11 Multiplexing and Demultiplexing
FDM – frequency division
WDM (wavelength division)
TDM – Time Division and variations.
Inverse multiplexing
CDM – code division