## Slide 1: Pipelining
Dr. John Abraham
Professor
UTRGV

## Slide 2: Pipelining defined
Multiple instructions are overlapped in execution
Divide the work of the cpu as equally as possible.
MIPS lends itself to pipelining because the only operations that affect memory are load and store and the instruction size is the same.
Clues taken from automobile assembly line. Person posted in each stage, must complete the work as the next one comes in. So each stage should take approximately same amount of time.

## Slide 3: Terminology
Pipe Stage - also a pipe segment, each step in a pipeline
Throughput - how often an instruction exits the pipeline
Machine cycle - time to move through 1 pipe stage
Stall - a situation in which a pipe stage requires more than 1 machine cycle to complete
  this freezes the pipe until that stage is done
Time per instruction on a pipelined computer:
  TPI = TPI unpipelined / number of pipe stages

## Slide 4: MIPS
32 registers
3 classes of instructions:
  ALU instructions
  Load and store instructions
  Branches and jumps
Implementation of one instruction takes 5 clock cycles
  Instruction Fetch (IF)
  Instruction Decode (ID)
  Instruction Execute (EX)
  Memory Access (MEM) in case of load/store
  Write-back (WB)

## Slide 5: 5 stages
IF – send the Program Counter to memory and fetch the current instruction. Update the PC by 4 bytes (why?).
ID – instruction decode and register fetch. Decode the instruction and read the operand registers from the register file. Compute branch target address by adding the offset to incremented PC, this is for branching.
EX – Memory reference operation for data in RAM. Register-Register Operation for data in Register. Register Immediate. One register and immediate
MEM. Calculate effective address and read. If write send it to effective address.
WB. Write the results into register file.

## Slide 6: MIPS Pipeline Datapath
  State registers between each pipeline stage to isolate them
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IFetch/Dec
Dec/Exec
Exec/Mem
Mem/WB
IF:IFetch
ID:Dec
EX:Execute
MEM:
MemAccess
WB:
WriteBack
System Clock
Sign
Extend
Notes: Note two exceptions to right-to-left flow
WB that writes the result back into the register file in the middle of the datapath
Selection of the next value of the PC, one input comes from the calculated branch address from the MEM stage
Only later instructions in the pipeline can be influenced by these two REVERSE data movements.
The first one (WB to ID) leads to data hazards.
The second one (MEM to IF) leads to control hazards.
All instructions must update some state in the processor – the register file, the memory, or the PC – so separate pipeline registers are redundant to the state that is updated (not needed).
PC can be thought of as a pipeline register: the one that feeds the IF stage of the pipeline. Unlike all of the other pipeline registers, the PC is part of the visible architecture state – its content must be saved when an exception occurs (the contents of the other pipe registers are discarded).

## Slide 7: Five-Stage Pipeline for MIPS

## Slide 8: Speed up realized
If all stages are balanced time for each instruction can be reduced by time it takes without pipelining divided by the number of stages. Pipeline rate is limited by the slowest stage.
Initial filling up and final emptying of pipeline will have to be added to the time. In a long program it would not matter much.
It follows, more the pipeline stages, the more speed up