## Slide 1: 6-Information Sources and Signals
Dr. John P. Abraham
Professor
UTRGV

## Slide 2: The Essence of Data Communication
Intersection of Physics, Mathematics and Electrical Engineering
  Current, light, other electro-magnetic radiation, digitization, Fourier transform, etc.
The source of information can vary, all using a single physical medium.
Sender – medium – receiver
Effective communication requires feedback

## Slide 4: Information Sources
Computer peripherals, microphones, sensors, measuring devices, etc.
Analog or Digital Signals
  Analog is continuous change
  Digital is discrete change at fixed intervals
Periodic and Aperiodic Signals
  Periodic repeats itself

## Slide 6: Sine waves and signal characteristics
Many natural phenomena occur in sine waves
  Electromagnetic radiation, sound, water waves, etc.
  There are 4 important characteristics of sine wave signals
    Frequency – the number of oscillations per second
    Amplitude - the difference between maximum and minimum signal heights
    Phase - How far start of the sinwave is shifted from a reference time
    Wavelength – length of a cycle (speed with which the signal propagates)

## Slide 8: Sine Wave
The sine wave or sinusoid is a mathematical function that describes a smooth repetitive oscillation. It occurs often in pure mathematics, as well as physics, signal processing, electrical engineering and many other fields. Its most basic form as a function of time (t) is:
where:
A, the amplitude, is the peak deviation of the function from its center position.
ω, the angular frequency, specifies how many oscillations occur in a unit time interval, in radians per second
φ, the phase, specifies where in its cycle the oscillation begins at t = 0.
  When the phase is non-zero, the entire waveform appears to be shifted in time by the amount φ/ω seconds. A negative value represents a delay, and a positive value represents a "head-start".

## Slide 9: Composite signals
    Most signals are classified as composite because the signals can be decomposed into several simple waves.
    Signals generated by modulation are usually composite.
    A mathematician named Fourier discovered that it is possible to decompose a composite signal into its constituent parts. Fourier transform is used to solve many problems in science and engineering

## Slide 10: Analog and Digital signals
Analog is characterized by continuous mathematical function. When input changes from one value to the next it does so by moving through all possible intermediate values.
Digital has a fixed set of valid levels, and each change consists of an instantaneous move from one level to another.

## Slide 11: Periodic and Aperiodic Signals
A periodic signal repeats the pattern.
Aperiodic does not repeat the pattern

## Slide 13: THEORETICAL BASIS FOR DATA COMMUNICATION
TRANSMIT ON WIRES BY VARYING PHYSICAL PROPERTY
  VOLTAGE
  CURRENT
  FREQUENCY
  PHASE
TRANSMIT ON GLASS FIBER BY SENDING LIGHT PULSES

## Slide 14: Data Rate
How much data can be sent in a given time? Depends on number of signal levels and time it remains in each signal level before going to the next.
If we reduce the time at each signal level, more data can be sent. But there is minimum to time required to detect the signal. Engineers measure the inverse: how many times the signal can change per second which is measured as baud. If signal remains for .001 sec, it is 1000 baud. If the system has 2 signal levels, then 1000 bits can be transmitted with 1000 baud. If it has 4 signal levels, 2000 bits can be transmitted.

## Slide 15: Bandwidth of analog and digital signals
Difference between the highest and lowest frequencies of constituent parts as yielded by Fourier analysis.
Digital signals: some systems use voltage to represent digital values. Only two levels of voltage indicate 0 or 1. Multiple levels of voltage may be used to indicate multiple bits.
-5 volt = 00, -2 volt = 01, +2 volt = 10, +5 volts = 11
If multiple levels are used electronics must be sensitive enough to distinguish between voltage levels.

## Slide 16: Bandwidth of a Digital signal
Applying Fourier analysis we find a digital signal has infinite bandwidth because a digital signal produce an infinite set of sine waves.

## Slide 19: Analog/Digital data
Digital Data to Digital Signals
Digital Data to Analog Signals
Analog Data to Digital Signals
Analog Data to Analog Signals

## Slide 20: Converting digital to analog.
Why do that? To transmit digital data over analog lines. Serial communication using modems. Basis of analog signaling is a continuous constant frequency known as the carrier signal.

## Slide 21: Digital Data to Analog Signals
ASK
FSK
PSK
Go to notes here to talk about modem, null modem, dce (data communication equipment), dte (data terminal equipment). Students must know these concepts.

## Slide 22: Digital Data to Digital Signals
Digital signal is a sequence of discrete discontinuous voltage pulses. Each pulse is a signal element. Unipolar  only positive voltage. Polar both positive and negative.
  NRZ
  Multilevel Binary
    Bipolar-AMI
    Pseudoternary
  Biphase
    Manchester and differential Manchester

## Slide 23: Non return to zero (NRZ) and NRZi
Easiest way to encode. Use 2 diff voltage levels. During a bit transmission the voltage does not return to zero
NRZi – non return to zero, invert on ones. No transition  zero. Transition one
In a twisted pair, if sending and receiving wires are improperly connected, nrzi is not affected. NRZ-I is an example of differential encoding. In decoding adjacent elements are compared for polarity changes.
Draw it on the board.

## Slide 24: Multilevel Binary
This technique uses more than two signal levels.
Bipolar AMI (alternate mark inversion)
A binary 0 is represented by no line signal. Binary 1 is represented by a positive or negative voltage. The binary ones must alternate in polarity. Draw it.
Advantage: no loss of synchronization in case of continuous one’s transmitted. Receiver can synchronize with each transmission.

## Slide 25: Biphase Manchester code
There is a transition at the middle of each bit period
This transition serves as a clocking mechanism. Low to hight represents 1 and high to low represents a 0.

## Slide 26: Ethernet Encoding
For 10 Mb/s Manchester Encoding. Idea is to detect a transition rather than voltage levels to define bits.
For 100 Mb/s NRZ-I and MLT-3.
For 1000 Mb/s - copper cable based Gigabit Ethernet (1000BASE-T), a pair of encoding methods was chosen, 8B1Q4 and 4D-PAM5. For fiber optic based Gigabit Ethernet (1000BASE-X), a different pair of encoding methods was chosen, 8B10B and NRZ.

## Slide 27: NRZ-i

## Slide 28: MLT-3
MLT-3 is an encoding method used on Fast Ethernet 100BASE-TX networks. It is similar to Manchester encoding in that a logic '1' is represented by a voltage transition. However, whereas a Manchester encoded signal uses a two-state waveform (0V or +V), an MLT-3 encoded signal uses a three-state waveform (-V or 0V or +V.)

## Slide 29: 8B1Q4 and 4D-PAM5 Encoding 0n 1000BASE-T
all four wire pairs must be used simultaneously in parallel when transmitting or receiving.
To achieve the 1000Mbps data rate, each wire pair must be able to transmit or receive at a data rate of 250Mbps.
the signal is first encoded using 8B1Q4 and then the 4D-PAM5 encoding method is applied after.

## Slide 30: Analog Data to Digital Signals
PCM – pulse code modulation DM-delta modulation .

## Slide 31: Encoding and Data compression
Lossy – some information is lost during compression JPEG MPEG
Lossless – all information is retained in the compressed version Repeated strings are compressed and a dictionary is created. Compressed data along with dictionary is sent to recreate the original data

## Slide 32: Analog Data to Analog Signals
AM
FM
PM