## Slide 1: THE IEEE MAC SUB-LAYER – chapter 14
Dr. John P. Abraham
Professor
University of Texas, RGV

## Slide 2: The data link layer (Layer 2 OSI)
LLC
  Logical Link Control
  Refers upward to higher layers
MAC
  Media Access Control
  refers downward to lower layers
Media Access
  Determine how to get access when there is competition for the media.
  MAC (Medium Access Control) sub-layer takes care of this problem
  MAC is important in LANs where broadcast channels are used
  MAC is the lower part of the data link layer (next to physical layer)
  Mac sub-layer does not guarantee delivery

## Slide 3: A Taxonomy of Mechanisms for Multi-Access
See the textbook for diagram p.242
1. Modified Form of Multiplexing Technique
2. Distributed Allgorithm for Controlled Access
3. Random Access Strategy

## Slide 4: Static Channel Allocation
Works well for situations where set of communicating entities known in advance and does not change (not good for cell phones)
Traditional way to allow more than one person to use the medium is to use FDM
In Frequency division multiplexing, the total band width is divided among the total number of users
FDM works well when there is a small number of users
When users grow a fast busy signal is issued

## Slide 5: Dynamic Channel Allocation
underlying assumptions of dynamic channel allocation
  1. Station Model
  2. Single Channel Assumption
  3. Collision Assumption
  4. Continuous time
  5. Slotted time

## Slide 6: Station Model
Consists of N independent STATIONS
Each has programs that produce frames for transmission
Frames are generated at intervals
Once a frame is generated the station is locked until the frame is transmitted

## Slide 7: Single Channel Assumption
Only one channel is available for all communication
All stations transmit on it and all stations receive on that channel

## Slide 8: Collision Assumption
If two frames are transmitted simultaneously, they overlap in time and resulting signal is garbled.
All stations can detect collisions.
A collided frame must be retransmitted.

## Slide 9: Continuous time
Frame transmission can start any time
There is no master clock controlling transmission (as opposed to slotted time discussed next)

## Slide 10: Slotted time
Time is divided into discrete intervals (slots)
Frame transmission begins at the start of a time slot

## Slide 11: Channelization Protocols
FDMA
TDMA
CDMA
Already discussed

## Slide 12: Controlled Access Protocols
Polling
  Using a centralized controller
  Round Robin or Priority Order
Reservation – as used in satellite system
Token Passing-> See next slides.

## Slide 13: 802.4 token bus
Each station knows the address of the station to its left and right
The highest numbered station may send the first frame
Then it passes permission to its immediate neighbor by sending a special frame called a token.
The first station passes the token to the highest numbered one.

## Slide 14: 802.5 token Ring
Physical Ring
Token circulates

## Slide 15: Random access /Multiple Access Protocols
ALOHA
  PURE ALOHA
  SLOTTED ALOHA
CARRIER SENSE MULTIPLE ACCESS PROTOCOLS (CSMA)
  Persistent and Nonpersistent CSMA
  CSMA with collision detection
Collision-Free Protocols
others

## Slide 16: ALOHA
1970 - Norman Abramson
University of Hawaii
Used ground based radio broadcasting. there are two frequencies: one for inbound and another for outbound.
Two versions of Aloha
  Pure
  Slotted

## Slide 17: Pure ALOHA
Users may send on the inbound frequency whenever they have data to send
The central transmitter repeats it in on the outbound frequency for all stations to hear
If collisions occur, collided data will be destroyed
Sender can determine if the data was destroyed by listening to the channel (the sender can hear too).
If data was destroyed, re-send after waiting random amount of time

## Slide 18: Slotted ALOHA
Divide time into discrete slots, each time slot is enough for one frame
Users agree on slot boundaries
A special station emits a signal at the start of each time slot to synchronize

## Slide 19: Carrier Sense Multiple Access Protocols (CSMA)
Standard for Ethernet known as DIX (Digital, Intel, Xerox – 1978)
Originally described by Xerox PARC researchers in 1973
Listen for a transmission
If the line is clear then transmit
Implementations:
  Persistent, Non Persistent and p-persistent
  CSMA with collision detection

## Slide 20: Persistent
Listen, if busy wait until line is free
Transmit a frame
If collision occurred, wait for a random amount of time
Transmission time delay between two sending computers will cause the second computer not to hear the transmission.

## Slide 21: Non-Persistent
Listen, if busy wait random amount of time and listen again until the line is free
This approach is less greedy than the Persistent one
This prevents two or more wanting to get on the line from doing so at the same time when the channel becomes free.

## Slide 22: P-persistent CSMA
Slotted channels.
Listen, if free send at the beginning of the next slot

## Slide 23: CSMA with Collision Detection (CSMA-CD)
Abort transmission as soon as collision is detected
Collision is detected by comparing received signal power to sent signal
If collision is detected, stop transmission and wait for random amount of time
CSMA/CD is used widely in LAN IEEE 802.3 is an example.

## Slide 24: Collision free protocols
Bit-map protocol
  A bit map with enough slots for all stations is passed around
  Each station wanting to send a frame and if the frame is ready in the que, inserts a 1 bit into its reserved slot in the bit map.
  Once station numbers of all who want to send is known they take turns in order.
Binary countdown

## Slide 25: Binary countdown protocol
Each station is given a binary address
If a station wants to transmit a frame it broadcasts its address one bit at a time starting with the high order bit.
Bits from each station are Ored together the station address starting with the resulting 0 or 1 bit is allowed to go on. If two or more has the same bit then go to the next bit and so on.

## Slide 26: CSMA/CA
Collision Avoidance instead of detection
For Wireless to avoid hidden stations
----A------B------C All can transmit but A may not detect Cs transmission, so if A and C transmit at the same time, there would be collision.
Solution: C says read to send. B says clear to send, which is heard by A and therefore backs off from transmitting. C now can send.